## Slide 1: Inverse and direct problems of optics: usage of artificial neural networks
Victor S. Abrukov
(2007)
e-mail: abrukov@yandex.ru
Chuvash State University, Russia
Department of Thermo Physics

## Slide 2: Chuvash State University, Russia
ChSU was founded in 1967. Over the last 30 years, the University has trained over 40,000 highly qualified specialists.
Main technological capabilities and facilities deal with physics, chemistry, electro engineering, thermo energetic, mechanical engineering and metalworking operation

## Slide 3: Outline
1. Introduction - 1
2. Artificial Neural Networks (ANN) Approach of Data Analysis
3. Introduction –2. Optical methods. Direct tasks and inverse problems
4. Goal of the work
5. ANN models for solving of direct and inverse problems of optics
5. Examples of Results Obtained and Perspectives
6. Conclusions

## Slide 4: Artificial neural networks (ANN) for new solutions of inverse and direct problems of optics
Abstract
Using the ANN we can calculate local and integral characteristics of object by means of incomplete set of data that characterize optical images (or signals)
Possibilities of usage the only value of a function of signal distribution in a plane of a registration in order to determine full distribution of local characteristics in an object as well as its integral characteristics are shown
It is very important for panoramic and integral optical methods but especially for optical fiber sensors and non-panoramic methods
Examples of ANN usage in the case of flame interferometry are presented.

## Slide 5: Introduction - 1
WORKING WITH
SOLUTION OF A PROBLEM,
IT IS USEFUL ALWAYS
TO KNOW AN ANSWER

## Slide 6: Artificial Neural Networks Approach of Data Analysis
Artificial neural networks (ANN) are computer codes training on examples
ANN use principles of human brain working, they are like children and need in training
ANN can be considered as a universal tool for multidimensional approximation.
The Kolmogorov-Arnold theorem dealing with capability of representation of multidimensional functions by means of superposition of functions of one variable is a basis of ANN application

## Slide 7: A part of human neural networks

## Slide 8: Scheme of human neuron

## Slide 9: Scheme of an artificial neuron
Artificial neuron consist of inputs, synapses, summator and non-linear converter, w- weights of a synapse (i = 1..., n); S - result of summation; xi - components of input vector (input signal); Y - output signal of a neuron; n - number of inputs of a neuron; F - non-linear transformer (function of activation).

## Slide 10: Artificial Neural Networks - 1
ANN represent some quantity of artificial “neurons” and can be presented often as “neurons” formed in layers (б).

## Slide 11: Artificial Neural Networks - 2
The input information goes on the first layer, then on the second layer and so on. After passing each layer, the information varies in accordance with synaptic weights of each neuron and its activation function.

## Slide 12: Artificial Neural Networks - 3
The task of ANN training consist of a finding such synaptic weights, at which ones the input information will correctly be mapped in outcome information
A database for ANN training can be formed by means of various techniques. An art of creation of a database is the first art of ANN technologies

## Slide 13: Introduction – 2. Optical metods
There are a lot of optical methods, for which a registered signal (light intensity) is the integral along light ray path in an object. Therefore they could be named as integral methods.
In some cases, these methods can be used to determinate both integral and local characteristics of objects.
Among them, following methods could be marked: interferometric technique, methods of video registration of radiation or absorption in various spectral bands, shadow methods, methods of small-angle scattering, absorption spectroscopy based on laser-diode, etc

## Slide 14: Introduction – 2. Direct tasks and inverse problems of optics
In order to determinate integral characteristics of object, these methods demand an integration of signal distribution in the plane of registration. It is a direct task.
In order to determinate local characteristics of object, these methods demand a solution of inverse problem of optics. To solve inverse problem is to solve integral equation, i.e. to determine an integrand by means of values of integrals.
Solution of both problems should be preceded by procedure of measurement of signal distribution in a plane of registration.
It is a difficult labor-intensive task and it is impossible task if an object cannot be registered (visualized) as a whole.

## Slide 15: Goal of the work
We would like to solve direct tasks and inverse problem of optics by means of ANN easy and fast
The main problem established in our work was to determine the integral and local characteristics of flame by means of ANN without necessity of measurement of large set of discrete values of the phases difference distribution function on the interferogram plane, S(x,y)
The solution of the problem is very important in real condition of physical experiments as well as for creation of automated systems of diagnostics and control in industry

## Slide 16: Example of ANN usage in a case of object with a cylindrical symmetry in a field of interferometry
Firstly let’s consider an inverse problem – a determination of integrand by means of incomplete set of integral meanings
We exam Abel integral equation for the case of cylindrical symmetry

## Slide 17: Objects with a cylindrical symmetry
! It is Important:
IF WE WILL BE ABLE TO SOLVE THE TASK WE SOLVE THE TASK FOR ALL OPTICAL METHODS THAT ARE INTEGRAL METHODS

## Slide 18: Method description - 1

## Slide 19: Method description - 2
where z2 + p2 = r2, z is a ray’s path in the object, p is an aim distance (0 < p < 1), r is a variable radius, n0 is a refractive index of undisturbed medium surrounding a flame and n(r) is a refractive index distribution in flame.

## Slide 20: Method description - 3
Using this equation, we can then calculate the integrals S(p) from different integrands of form nо – n(r) = 1 + ar – br2, where a and b are the given constants and thus to create a data base consist of various S(p) and integrands.
In total we used seven different integrands that reflect a real distribution of refractive index distribution in flames

## Slide 21: Method description – 3.1

## Slide 22: Method description - 4
The ANN training data base was obtained as follows. For various r, values nо – n(r) were calculated. Then the integrals of each of these seven integrands were calculated. For example, for the function nо – n(r) = 1 + 4r – 5r2, we can obtain the following expression

## Slide 23: Method description - 5
Then the values of S(p) are calculated for different p. The input data for training the NNW were values of S(p), p and r. Values of integrand corresponding to each radius are the target (output) values. In total, we used about 700 sets of these parameters.

## Slide 24: Distribution of local characteristics. Training of ANN and creation of ANN model
Data base of input values for training
S, p, and r
Neural Networks Wizard 1.7
(or the Data Fusor - at present time )
Output values
n(r), T(r), etc

## Slide 25: Structure of the ANN used for solving inverse problem (n = nо – n(r))

## Slide 26: Method description – 6 . “Back propagation of error”

## Slide 27: Method description - 6
During testing, values of S(p), p and r are installed on input of NNW and values of nо – n(r) obtained are compared with precise values of a function. The results of testing of the NNW (relative error) for an integrand nо – n (r) =1 + 0.5r – 1.5r2 (that have not been used for training of NNW) and two values of aiming distance p=0.1 and p=0.8 as well as average relative errors of integrand calculated in the interval of p between 0.1 up to 0.9 are represented in Fig. 2.

## Slide 28: Relative errors of the ANN integrands calculation - 1

## Slide 29: Relative errors of the ANN integrands calculation - 2

## Slide 30: An interferogram of a real flame

## Slide 31: Table 1. Results obtained and errors in a case of real flame
r
n0-n(r)
estimated by classical method (full data about S(p))
n0-n(r)
estimated by ANN (one point of S(p))
Errors, %
0
0,0002
0,00021
5,08
0,1
0,000207
0,000198
4,35
0,2
0,000208
0,000195
6,25
0,3
0,000203
0,000186
8,37
0,4
0,000192
0,000174
9,38
0,5
0,000175
0,000168
4,05
0,6
0,000152
0,000149
1,97
0,7
0,000124
0,000129
4,03
0,8
0,000088
0,000095
7,95
0,9
0,000048
0,000052
8,33

## Slide 32
Integral characteristics. Training of ANN and creation of ANN model
Data base of input values for training
S and p
Neural Networks Wizard 1.7
(or the Data Fusor - at present time )
Output values
H, m, F, etc

## Slide 33: Error in a case of determination of flame heat quantity

## Slide 34: Outputs
The results show the ANN can solve the inverse and direct problem of optics easy and fast with an acceptable accuracy in a case of cylindrical symmetry.
Further perspectives of the work are concerned with the implementation of neural networks for solving the inverse and direct problems for other optical methods, other kinds of symmetry and also for solving the practical problems of testing and control.

## Slide 35: Perspectives - 1
Before (without ANN): Approximately 1 hour for measurements about 50 …100 values of S(xi,yi) in plane of whole interferogram.
In the nearest future (with ANN): Approximately 1 sec. for doing a mouse click on an interferometric band of a part of interferogram

## Slide 36: Perspectives – 2. Shape, Size and Orientation of Object. Recognition and determination by ANN
In a case of homogeneous object, the ANN allow to define a form, size and orientation of an object by means of measurement of the only value of a function of signal distribution in a plane of the registration (for example for X-ray diagnostics).
In this case, the input data for training the ANN can be values of signal intensity I(p) and p. Values of form (in a sense of form category), size and orientation (in a sense of angle) will be a target values.
Preliminary results obtained by us show the ANN solves the tasks of recognition of circle, ellipse, four-square and rectangle very well.

## Slide 37: Conclusions
The ANN can allow to solve number of tasks that could not be solved by means of usual approaches.
The determination of one integral value (and also it changes during time in case of non-stationary objects) can be automated. Therefore it is possible to use a ANN-like chip (microprocessor) embedded into automated control systems.
Further perspectives of the work are concerned with the implementation of neural networks for solving the inverse and direct problems for other optical methods and also for solving the practical problems of testing and control.

## Slide 38: Industry perspectives
1. Novel methods and devices for diagnostics, testing and control (optical fiber sensors, smart sensors and MEMS);
2. New ways for creation of industry systems of testing and control.

## Slide 39: References
1. Abrukov V.S., Ilyin S.V., Maltsev V.M., and Andreev I.V.: Proc. VSJ-SPIE Int. Conference, AB076 (1998). http://www.vsj.or.jp/vsjspie/
2. Abrukov V.S., Andreev I.V., Deltsov P.V.: Optical Methods for Data Processing in Heat and Fluid Flow. Professional Engineering Publishing, London (2002), p. 247 - 266
3. Neural Networks for Instrumentation, Measurement and Related Industrial Applications. Proceedings of the NATO Advanced Study Institute on Neural Networks for Instrumentation, Measurement, and Related Industrial Applications (9-20 October 2001, Crema, Italy)/ Ed. by Sergey Ablameyko, Liviu Goras, Marco Gori and Vincenzo Piuri, IOS Press, Series 3: Computer and Systems Sciences – Vol. 185, 2003. – 329 pp.
4. The BaseGroup Laboratory: http://www.basegroup.ru
5. Abrukov V.S., Smirnov V.E., Ivanov D.G. Applications of Digital Image Processing XXVII/ Ed. Andrew G. Tescher. Proc. of the 49th SPIE’s Meeting (2004, 2-6 August, Denver, CO, USA), SPIE, Bellingham, WA, 2004, Vol. 5558.
6 Abrukov V.S., Pavlov R.A., Malinin G.I. Inverse and direct problems of optics: usage of artificial neural networks. In: Proc. of the 49th SPIE’s Meeting (2004, 2-6 August, Denver, CO, USA), 2004, Vol. 5531, pp. 285-288.
7 Abrukov V.S., Deltsov V.P., Pavlov R.A Inverse and direct problems of combustion diagnostics and artificial neural networks. In: Book of the Ninth International Workshop (9-IWCP) on Novel Energetic Materials and Applications/ Ed. by Luigi T. DeLuca, Rose Ann Pesce-Rodriguez, 2004, paper 25, pp. 1-11.

## Slide 40: Conclusion 2
All you need in your life is love
All you need in your scientific life is neural networks
It can be artificial neural networks